## Slide 1: MODULE III SYSTEM MODELS
System Models - Building blocks of Mechanical, Electrical, Fluid and Thermal Systems, Modeling spring, mass & damper systems, Rotational –Translational Systems, Electromechanical Systems, Hydraulic –Mechanical Systems.

## Slide 2: INTRODUCTION
How do a system behave w.r.t time when subject to some disturbances?????
It takes time to resume to required state
Eg: motor starts to rotate in full speed only after a time – it takes time to fill required tank level when tap is opened

## Slide 3: CONT..
MATHEMATICAL MODEL
a model is required – represent real behavior of a system
Mathematical model – equation – describing relation between input & output of a system
base for this mathematical model???
Fundamental physical laws – governs – the behavior of the system

## Slide 4: BUILDING BLOCKS
A block that is used to build up a system
Single property or function
Eg: an electrical system may consist of resistor, inductor & capacitor – resistor is a separate block that has property of resistance – likewise capacitor & inductor are different blocks having property of storing & inducing charges respectively

## Slide 5: Cont…
Mechanical
Electrical
Fluid
Thermal

## Slide 6: LUMPED PARAMETERS
Eg: an electrical system may consist of resistor, inductor & capacitor – resistor is a separate block that has property of resistance – likewise capacitor & inductor are different blocks having property of storing & inducing charges respectively
Number of electrical circuits can be formed by combining these building blocks in different way
Lumped parameter – system formed by different blocks – these blocks are independent

## Slide 7: MECHANICAL BUILDING BLOCKS
Models – represent mechanical systems
Mechanical system – made up of spring/dashpot/mass – or contains their property alone without real spring/dashpot/mass
Input – force & output - displacement
BLOCK | PHYSICAL REPRESENTATION
SPRING | Stiffness of a system
DASHPOT | Forces opposing the motion (ie) friction / dampness effect
MASS | Inertia or Resistance to acceleration

## Slide 8: SPRING
F = k . x
F- force to compress / extend the spring
k - stiffness
Due to the input force, spring exerts equal force called as spring force but in opposite direction due to Newton’s 3rd law of motion

## Slide 9: DASHPOT
To push an object through a fluid or move an object against frictional forces
F = c . v
c – damping coefficient
Due to the input force, dashpot exerts equal force called as dashpot force but in opposite direction due to Newton’s 3rd law of motion

## Slide 10: MASS
a - acceleration
Mass always moves in the direction of input force

## Slide 11: ENERGY OF MECHANICAL BUILDING BLOCK
=
Spring
Stores energy & release when returned to original position
Mass
Stores energy (kinetic energy) & releases when stops moving
Dashpot
No energy stored & do not return to its original position – dissipates energy - power

## Slide 12: ROTATIONAL SYSTEM
Spring
Mass
Dashpot
Torsional Bar / Torsional spring
Moment of Inertia
Torsional Damper / Rotary Damper

## Slide 13: Cont…

## Slide 14: BUILDING A MECHANICAL SYSTEM
Machine mounted on the ground,
The chassis of a car moving with wheel on road
The driver of a car while driving in the road

## Slide 15: STEPS TO SOLVE PROBLEMS
Draw a free body diagram of each mass with the forces associated with it ( spring force & dashpot force are always in opposite direction to input force F )
Write the net force acting on the mass
  Sign convention: +ve sign for left to right forces - bottom to top forces - clockwise forces
Apply Newton’s Second law of motion
NET FORCE = m . a = m . d2x/dt2

## Slide 16: DERIVE AN EQUATION TO RELATE INPUT FORCE F WITH OUTPUT DISPLACEMENT ( X Or )
Refer Notes for Derivation

## Slide 17: CONT…
Refer Notes for Derivation

## Slide 18: CONT…
Refer Notes for Derivation

## Slide 19: ELECTRICAL BUILDING BLOCKS
BLOCK | PHYSICAL REPRESENTATION
RESISTOR | Opposition to movement
CAPACITOR | Store charge
INDUCTOR | Inducing voltage due to change in magnetic field of coil
Models – represent electrical systems
Input – applied voltage & output – voltage across any block given

## Slide 20: RESISTOR
VR– voltage across resistor ; i – current ; R – resistance ; PR – power dissipiated
Potential difference across α current

## Slide 21: CAPACITOR
VC – voltage across capacitor ; i – current ; C – capacitance ; EC – energy stored
Potential difference across α charge

## Slide 22: INDUCTOR
VL – voltage across inductor ; i – current ; L – inductance ; EL – energy stored
Potential difference across α rate of change of current

## Slide 23: ANALYSIS OF ELECTRICAL SYSTEM
KIRCHOFF’S LAW
  Current law – algebraic sum of current at a junction is equal to zero. (more than one loop)
  Voltage law – in a loop sum of voltage across each part is equal to applied voltage. (single loop)

## Slide 24: STEPS TO SOLVE PROBLEMS
Draw the circuit diagram
Input is applied voltage (v) & output will be given in the question as Vc (voltage across capacitor) or VR (voltage across resistor) or VL (voltage across inductor)
  If single loop :
    use voltage law (
    Convert VR , VL, Vc everything in terms of current equation & then substitute i current with output voltage ( for example if output voltage is VC then write all i interms of VC )

## Slide 25: CONT…
  If more than one loop:
    Use current law ()
    Convert all i (current) in the equation in terms of output voltage suitably
  Rearrange all the terms in such a way input voltage on one side & output voltage on other side

## Slide 26: DERIVE A RELATION BETWEEN INPUT VOLTAGE AND OUTPUT VOLTAGE
Refer Notes for Derivation

## Slide 27: CONT…
Refer Notes for Derivation

## Slide 28: ELECTRICAL & MECHANICAL ANALOGY
Spring
Mass
Dashpot
Inductor
Capacitor
Resistor

## Slide 29: FLUID BUILDING BLOCK
Hydraulic – liquid – incompressible
  Relation between pressure / height and volumetric flow rate
Pneumatic – gas - compressible
  Relation between pressure and mass flow rate

## Slide 30: HYDRAULIC BUILDING BLOCKS
BLOCK | PHYSICAL REPRESENTATION
HYDRAULIC RESISTANCE | Opposition to flow
HYDRAULIC CAPACITANCE | Store as potential energy
HYDRAULIC INERTANCE | Accelerate a fluid by pressure difference

## Slide 31: HYDRAULIC RESISTANCE
P1 & P2 – pressure @ 1 & 2
q – volume flow rate
R – hydraulic resistance
PR – power dissipiated
Orifices, valves, nozzles and friction in pipes can be modeled as fluid resistors

## Slide 32: HYDRAULIC CAPACITANCE
q1 & q2 – volume flow rate @ inlet & outlet
P1 & P2– pressure @ 1 & 2
C – hydraulic capacitance
EC – energy stored
C
Refer Notes for Derivation
Hydraulic cylinder chambers,
tanks, and accumulators are
examples of fluid capacitors

## Slide 33: HYDRAULIC INERTANCE
q1 & q2 – volume flow rate @ 1 & 2
P1 & P2– pressure @ 1 & 2
C – hydraulic inertance
EI – energy stored
Refer Notes for Derivation
Long pipes are examples of fluid
inertances

## Slide 34: PNEUMATIC BUILDING BLOCKS
BLOCK | PHYSICAL REPRESENTATION
PNEUMATIC RESISTANCE | Opposition to flow
PNEUMATIC CAPACITANCE | Store as potential energy
PNEUMATIC INERTANCE | Accelerate a gas by pressure difference

## Slide 35: PNEUMATIC RESISTANCE
ṁ
P1 & P2 – pressure @ 1 & 2
ṁ – mass flow rate
R – pneumatic resistance
PR – power dissipiated
Orifices, valves, nozzles and friction in pipes can be modeled as fluid resistors

## Slide 36: PNEUMATIC CAPACITANCE
ṁ1 & ṁ2 – mass flow rate @ inlet & outlet
P1 & P2– pressure @ 1 & 2
C1 – pneumatic capacitance (change in volume)
C2 – pneumatic capacitance (compressibility)
EC – energy stored
Refer Notes for Derivation
Hydraulic cylinder chambers,
tanks, and accumulators are
examples of fluid capacitors

## Slide 37: PNEUMATIC INERTANCE
ṁ1 & ṁ2 – mass flow rate @ 1 & 2
P1 & P2– pressure @ 1 & 2
I – pneumatic inertance
EI – energy stored
Refer Notes for Derivation
Long pipes are examples of fluid
inertances

## Slide 38: Derive a relation for height of the tank (change in flow rate is slow / neglect inertance)
Refer Notes for Derivation

## Slide 39: DERIVE A RELATION FOR THE FLUID LEVEL IN TWO CONTAINERS ( CHANGE IN FLOW RATE IS VERY SLOW )
Refer Notes for Derivation

## Slide 40: DERIVE A RELATION FOR THE VARIATION ON PRESSURE 2 DUE TO PRESSURE 1 ( CHANGE IN FLOW RATE IS VERY SLOW )
Refer Notes for Derivation

## Slide 41: THERMAL BUILDING BLOCKS
BLOCK | PHYSICAL REPRESENTATION
THERMAL RESISTANCE | Opposition to flow of heat
THERMAL CAPACITANCE | Store of internal energy

## Slide 42: THERMAL RESISTANCE
q
T1 & T2 – temperature @ 1 & 2
q – rate of flow of heat
R – thermal resistance
k – thermal conductivity
h – coefficient of heat transfer
A – area of cross section
L length of pipe
CONDUCTION
CONVECTION

## Slide 43: THERMAL CAPACITANCE
C.T
q1 & q2 – heat flow rate @ inlet & outlet
T– temperature
C – thermal capacitance
m – mass of the object
c – specific heat capacity
EC – energy stored
C

## Slide 44: DERIVE A RELATION BETWEEN THE TEMPERATURE OF THERMOMETER AND LIQUID
Refer Notes for Derivation

## Slide 45: DERIVE A RELATION TO SHOW HOW THE ROOM TEMPERATURE CHANGES WITH TIME
Refer Notes for Derivation

## Slide 46: COMBINED BUILDING BLOCK
Many systems in real life involves combination of more than one discipline:
  rotational & translational building blocks (Eg: rack & pinion)
  Electrical & mechanical building blocks (Eg: potentiometer , dc motor)
  Hydraulic & mechanical (Eg: movement of piston by a valve)
Refer Notes for Derivation